Raspberry Pi and Perl

---
What is this thing?
- Small, cheap computer
- System-on-a-chip, includes CPU, GPU, RAM
- A few options for OS
  - We'll focus on Linux
- First intended to teach kids to program
  - Developers thought modern computers to complicated
- Became popular among hardware hackers

---
Raspberry Pi Hardware
(Model B4)
- ARM A72, quadcore, 64-bit, 1.5GHz
- 1GB/2GB/4GB RAM (1GB no longer made)
- GPU
- 2x USB2.0, 2x USB3.0
- 2xHDMI mini ports
- Gigabit Ethernet
- MicroSD card for OS and storage
- USB-C port for power (need 3A)
- Optional camera

---
Other Single Board Computers
- Raspberry Pi Zero – Small form factor, cheap
- Rock Pi S – Cheap, more capable than Zero
- Banana Pi – Various models, some with M.2 storage
- Nvidia Jetson Nano – Higher performance, >$100
- Why bother with Raspberry Pi?
  - Stability
  - Community support

---
SD Cards
- Primary storage for the Rpi
- Older SD speed classes about sequential read/write
- Rpi needs random read/write
- Good class 4 cards can be better than cheap class 10
  - . . . but now look for A1/A2 cards
  - Pi 3 or lower may not make use of A2 speeds
  - Can the Pi 4?

---
Raspberry Pi Software
- Many types of OS, but Raspbian most popular
  - Debian distro
- Very easy setup, just copy files to SD card
- Perl already installed
- RPi modules interface to hardware
- Older stuff might use HiPi modules

---
Peripheral Interface

---
Blink an LED
- "Hello, world!" of hardware projects
- If you can turn on an LED, you can turn on anything (digitally)
  - Use a relay or MOSFET for high-powered things

---
LED Blink Circuit

---
LED Blink Code
#!perl
use v5.20;
use RPi::WiringPi;
use RPi::Const qw(:all);
my $pi = RPi::WiringPi->new;
my $pin = $pi->pin( 2 );
$pin->mode( OUTPUT );
my $set = 0;
while(1) {
    $pin->write( $set );
    $set = ! $set;
    sleep 1;
}

---
Demo LED Blink

---
Input From a Switch
- Also seems trivial
- Pullup resistors
  - Let you reliably get the state of the button
  - Inverts the state—0 is on, 1 is off

---
Switch Circuit

---
Switch Input Code
#!perl
use v5.20;
use RPi::WiringPi;
use RPi::Const qw(:all);
use Time::HiRes 'sleep';
my $pi = RPi::WiringPi->new;
my $pin = $pi->pin( 2 );
$pin->mode( INPUT );
$pin->mode( PUD_UP );
while(1) {
    say $pin->read ? "High" : "Low";
    sleep 0.1;
}

---
Dim an LED
- Pulse Width Modulation (PWM)
- Turning on and off really fast
  - If it's on 50% of the time, looks 50% as bright
  - Handled by hardware with simple programming
- Can also be used on motors
- Frequency matters
  - See: Cheap LED christmas lights
  - Raspbery Pi's default seems fine
- Set value between 0 and 1023

---
PWM Signals
255
768

---
PWM Code Header
#!perl
use v5.20;
use RPi::WiringPi;
use RPi::Const qw(:all);
use Time::HiRes 'sleep';
my $pi = RPi::WiringPi->new;
my $pin = $pi->pin( 12 );
$pin->mode( PWM_OUT );

---
PWM Code Loop
my $set = 0;
my $is_going_down = 0;
while(1) {
    $pin->pwm( $set );
    if( $is_going_down ) {
        if( $set > 0 ) {
        $set--;
        }
        else {
        $set++;
        $is_going_down = 0;
        }
    }
    else {
        if( $set < 1023 ) {
        $set++;
        }
        else {
        $set--;
        $is_going_down = 1;
        }
    }
    sleep 0.001;
}

---
PWM Demo

---
Communication
- Arduino
  - More PWM channels (6 vs 1)
  - Servo library (motor control)
  - Real time
- Other devices
  - GPS
  - Accelerometers

---
UART
- Good ol' serial connection
- 2 wires to connect
- Rpi can also configure serial terminal over its UART pins
  - Be sure to turn that off if you want to use it programmatically
- Can also get USB adapters

---
SPI
- Serial Peripheral Interface
- Not a real standard
- 5 wires to connect
- Master/slave devices
- Raspberry Pi refuses to be a slave
- AVR can be a slave, but Arduino library won't

---
I²C
- Inter-Integrated Circuit
  - Sometimes called "TWI"--Two Wire Interface
  - Or SMBus
- Real standard, originally by Phillips Semiconductor, relatively open
- On tons of stuff
- 2 wires to connect (and ground)

---
I²C TMP102 Temperature Sensor
#!perl
use v5.20;
use warnings;
use RPi::WiringPi;
use RPi::Const qw{ :all };
my $rpi = RPi::WiringPi->new;
my $tmp102 = $rpi->i2c( 0x48 );
while(1) {
    my $temp = $tmp102->read_bytes( 2, 0x00 );
    say "${temp}C";
    sleep 1;
}

---
Questions?