Raspberry Pi and Perl

---
What is this thing?
- Small, cheap computer
- System-on-a-chip, includes CPU, GPU, RAM
- A few options for OS
  - We'll focus on Linux
- First intended to teach kids to program
  - Developers thought modern computers to complicated
- Became popular among hardware hackers

---
Raspberry Pi Hardware (Model B)
- ARM-on-a-chip (Broadcom BCM2835)
- 512 MB RAM
- GPU
- 2x USB Ports
- HDMI, RCA video
- Ethernet
- SD card for OS and storage
- USB micro port for power (need ~700mA)
- Optional camera

---
Camera Module
- Optional perpherial
- Better than your average web cam
- 5MP Native Resolution (2592x1944)
- Video, 1080p30, 720p60, 640x480p60/90
- Can access through external program for now
  - (Working on direct Perl access)

---
Raspberry Pi Software
- Many types of OS, but Raspbian most popular
  - Debian distro
- Very easy setup, just copy files to SD card
- Perl already installed
- HiPi modules interface to hardware

---
Peripheral Interface

---
Project Ideas
- Internet Garage-door
- Security camera
- Home web server
- Time-lapse video
- Sensor logging
  - Humidity
  - Temperature

---
Blink an LED
- "Hello, world!" of hardware projects
- If you can turn on an LED, you can turn on anything (digitally)
  - Use a relay for high-powered things

---
Demo Blinking LED

---
Run LED When Hitting a Switch
- Also seems trivial
- If you can run an LED based on input, you can run anything based off any (digital) input
- Pullup resistors
  - Let you reliably get the state of the button
  - Inverts the state—0 is on, 1 is off

---
Demo Input

---
Dim an LED
- Pulse Width Modulation (PWM)
- Turning on and off really fast
  - If it's on 50% of the time, looks 50% as bright
  - Handled by hardware with simple programming
- Can also be used on motors
  - But not RC hobby ESCs
- Frequency matters
  - See: Cheap LED christmas lights
  - Raspbery Pi's default seems fine

---
Demo PWM

---
Communication
- Arduino
  - More PWM channels (6 vs 1)
  - Servo library (motor control)
  - Real time
- Other devices
  - GPS
  - Accelerometers

---
SPI
- Serial Peripheral Interface
- 5 wires to connect
- Master/slave devices
- Raspberry Pi refuses to be a slave
- AVR can be a slave, but Arduino library won't

---
UART
- Good ol' serial connection
- 2 wires to connect
- USB port on Arduino is connected to this
  - Same thing used for loading program
  - Also used for logging
  - Different uses interfere with each other

---
I2C
- Inter-Integrated Circuit
  - Hardware interface called "TWI"--Two Wire Interface
- 2 wires to connect (and ground)
- Most Arduinos are 5V, Raspberry Pi is 3.3V
  - Can buy a "leveler"
- Need to unblacklist and install some Linux modules

---
I2C Program